## Slide 1
Applications of FEWS NET Remote Sensing Products for Agro-climatological Analysis — Snow Monitoring
Shahriar Pervez
U.S. Geological Survey
spervez@usgs.gov

## Slide 2: Snow Product Inventory
Snow Cover – provides us the areal extent of snow on the ground.
Snow Depth – provides us how deep the snow is on the ground.
Snow Water Equivalent – provides us how much of liquid water available in the snow we have on the ground.
Streamflow – tells us where does the water go when it starts to melt.
What’s common among these four?
They involve processes on the land surface
Measures of water availability

## Slide 3: What Drives the Process and Change?
Global water cycle
Upstream, Midstream, and Downstream regions of a River catchment.
Why don’t we get same amount of rain and snow every season/year?

## Slide 4: What Drives the Processes and Change?
Walker Circulation
Hadley Circulation

## Slide 5: What Drives the Processes and Change?
Indian Ocean Dipole
Neutral
Negative
Positive

## Slide 6: Monitoring of Snow

## Slide 7: Ways to Monitor Snow
Snow — snow is a form of precipitation within the Earth’s atmosphere in the form of ice crystals that fall form the clouds. When temperatures drop below 0°C and there is sufficient humidity in the atmosphere, water vapor condenses directly into ice without going through the liquid stage. Once an ice crystal has formed, it absorbs and freezes additional water vapor from the surrounding air, growing into a snow crystal or snow pellet, which then falls to Earth because of the gravity.
In-situ measurements
Remote sensing
Land surface hydrology modeling

## Slide 8: In-situ Measurements of Snow
Snow Tubes/depth gage for depth estimation
Snow pillows for snow water equivalent estimation
Snow Lysimeters for snow melt estimation
Meteorological Towers for local atmospheric condition estimates

## Slide 9: Remote Sensing of Snow
Remote sensing — it is the process of detecting and monitoring the physical characteristics of an area by measuring reflected and emitted radiation at a distance typically from satellite or aircraft.
All matters at temperature greater than absolute zero (0° K or -273° C) continuously emit EMR
Solar EMR is reflected from surface-to-sensor
Absorbed by surface and then emitted from surface-to-sensor.
reflective
emitted

## Slide 10: Spectral Signature of Snow
MODIS Image over Afghanistan

## Slide 11: Production of MODIS Snow Cover Extent
MODIS scans the entire globe every one to two days. As such, most locations on Earth are imaged at least once per day.
The MODIS instrument provides 36 spectral bands ranging in wavelength from 0.4 μm to 14.4 μm. Two bands are imaged at a nominal resolution of 250 m at nadir, five bands at 500 m, and the remaining bands at 1000 m.
Snow cover is detected using the Normalized Difference Snow Index (NDSI). Snow-covered land typically has very high reflectance in visible bands and very low reflectance in shortwave infrared bands; the NDSI reveals the magnitude of this difference.
Typically, it takes five to seven days to reach a nearly cloud free map, thus 8-day composite is created.
The snow cover is created, archived and distributed by NASA National Snow and Ice Data Center.
USGS downloads the data, clips it to Afghanistan extent, and them creates the maps.
3 459–479 Shortwave/VIS
4 545–565 Shortwave/VIS
5 1230–1250 Shortwave/NIR
6 1628–1652 Shortwave Infrared/SWIR
7 2105–2155 Shortwave Infrared/SWIR
MODIS 500 m bands and their wavelengths

## Slide 12: What Does SCEM Show?
Historical average for the month
Previous period
Previous year

## Slide 13: Snow Cover Depletion Computation
Download the MODIS snow cover data for the dates you would like to compute the snow cover change
Use Clip Raster in ArcGIS Pro to clip the data for Afghanistan based on Province or Basin layer.
Raster value 200=Snow
Run a Con (conditional statement) to separate snow cells only.
CellValue = 200
Run Polygon to Raster to create a raster with the Province or Basin layer matching the same cell size and cell alignment with clipped snow layer. This would be your Zone to summarize snow extent for.
Out put raster would be all the snow cells over Afghanistan.

## Slide 14: Snow Cover Depletion Computation
Run Zonal Statistics as Table using the Zone and only Snow Cells layers as inputs to summarize how many snow cells are within each zone. Zone would be either Provinces or Basins and Snow Cells layer would be the daily MODIS snow cover extent.
Run the Zonal Statistics as Table for all the dates you would like to use for snow depletion computation.
Snow cover over Helmand during Jan 1-8, and Jan 9-16, 2025 were:
Or
Snow cover reduced in Jan 9-16, 2025 period

## Slide 15: Snow Cover Extent
Let’s check it on the https://earlywarning.usgs.gov/fews/search

## Slide 16: Remote Sensing of Snow Depth & SWE
Passive Microwave remote sensing — it is the process of detecting natural microwave energy emitted by objects or surfaces on the Earth. Passive microwave sensors typically measure thermal radiation emitted by the objects or surfaces at frequencies between 1 and 100 GHz.
However, microwave radiation energy level emitted from the Earth objects or surfaces are very low. This low energy levels make it difficult to measure small areas in detail. To measure a detectable level of energy the spatial resolution needs to be coarse (15km to 100km).
This is why microwave data (such as SSM/I, AMSR-E) or derivative products typically do not serve the purpose of FEWS NET, thus not used for FEWS NET.

## Slide 17: Modeling of Snow and Streamflow

## Slide 18: FEWS NET Land Data Assimilation System
97,597 total cores
8.1 PetaFlop/S
IBM GPFS
49.5 PB Disk
Operating System: SLES
Job Schedular: Slurm
Compilers: C, C++, Fortran
Discover

## Slide 19: FLDAS Outputs
Snow Depth – provides us how deep the snow is on the ground.
Snow Water Equivalent – provides us how much of liquid water available in the snow we have on the ground.
Streamflow – tells us where does the water go when it starts to melt.
Soil Moisture – provides us how much of water available at 4 different soil layers.

## Slide 20: Snow Depth
Snow depth — it is the average depth of snow over a 1 km x 1 km area and gets updated daily.

## Slide 21: Snow Depth
Let’s check it on the https://earlywarning.usgs.gov/fews/search

## Slide 22: Snow Water Equivalent (SWE)
Snow water equivalent — it is the amount of liquid water available in the snow. Snow depth is measured in meters whereas SWE is measured in water volume such as cubic meters or cubic kilometers. Air temperature is the primary factor in determining how much water is held in the snow. Colder temperatures produce lighter, fluffier snowflakes containing less water per centimeter of snow, while warmer temperatures near freezing create heavier, wetter snowflakes with a higher water content.
snow
water

## Slide 23: Snow Water Equivalent (SWE)
SWE — availability of liquid water over a 1 km x 1 km area and gets updated daily.

## Slide 24: How to Compute SWE
250
300
350
150
199
160
26
10
125
26
59
86
158
58
25
10
6
57
In Kg m-2
36
86
Average 180.3 kg m-2
or
180.3/1000 = 0.1803 m of water
2. Total area = 20 cells * cell resolution
3. Our cell resolution is 1 km x 1 km
or
1000 m x 1000 m
What was the total volume of water?
= 0.1803 m x 1000 m x 1000 m x 20
= 3,606,000 m3
= 3,606,000 / 1,000,000 million m3
= 3.6 million m3
On Jan 14 of 2025
Zonal average
999.97246766225 or roughly 1000 Kg m-2 = 1 m of water

## Slide 25: SWE Curve
SWE curve — progression of SWE at a regular interval e.g. daily.

## Slide 26
Difference Between SWE and SWE Curve
SWE – a snapshot of water availability
SWE curve – an evolution of seasonal water availability over an area (basin)

## Slide 27
Water Availability in Dam Basins
Dams in Afghanistan
Dam catchment or upstream area

## Slide 28: SWE Tool on Early Warning Explorer (EWX)
Let’s check it on the https://earlywarning.usgs.gov/fews/software-tools/1

## Slide 29: What Happens when Snow Starts to Melt
The top of the saturated zone in the soil (the water table) is deep, so percolating meltwater infiltrates to raise the water table and induce increased groundwater flow to the stream.
The water table is at the soil surface, of the soil surface is impermeable (the ground may be still frozen), so percolating meltwater forms a basal saturated zone through which water migrates to the stream.
The lower portion of the water table has risen above the ground surface into the snowpack. Water in the upper part of the slope infiltrates to raise the water table and percolating water in lower part forms basal saturated zone then migrates to the stream.

## Slide 30: Streamflow
NOAH 3.6/NOAH-MP + HyMAP2
Streamflow — it is the amount of water flowing in a river, it also refers as discharge. Typically, a hydrograph is used to study streamflow. A hydrograph is a chart showing most often streamflow/discharge (amount of water crossing a section of the river e.g. cubic meter per second) or river stage (height of the water above an arbitrary altitude e.g. MSL).
Bankfull — it is the water stage at which a river is at the top of its banks and any further rise in water state would result in water moving into the flood plain.
Return period — it is the average number of years between floods of a certain size. It is to compare how common some floods are annually.

## Slide 31: Streamflow Monitoring
Streamflow monitoring system for Flood early warning

## Slide 32: Streamflow Monitoring
Runoff based flood early warning

## Slide 33: Flood Early Warning
Let’s check it on the https://earlywarning.usgs.gov/fews/search/Asia/Central%20Asia/Afghanistan

## Slide 34: Snow Water Volume Assessment

## Slide 35: Analog Year
Water year is October to September
A total of 10 analog years were identified by Andy Hoell of NOAA, they are as follows:
2000-01, 2003-04, 2005-06, 2007-08, 2010-11, 2017-2018, 2020-2021, 2021-2022, 2022-23, 2023-2024
Out of this list of weak La Niña years, average to below average rainfall were used for SWE.
They are: 2005-06, 2017-18, and 2022-23

## Slide 36: Analog Years
La Niña Analog Years: 2000-01, 2003-04, 2005-06, 2007-08, 2010-11, 2017-2018, 2020-2021, 2021-2022, 2022-23, 2023-2024
El Niño Analog Years: 2004-05, 2006-07, 2009-10, 2010-11, 2014-15, 2016-17, 2018-19

## Slide 37: Helmand
This figure with all identified La Niña years of SWE is to look at the typical signal of SWE during the La Niña years.
It suggests, while early spring (Jan-Mar) might be ok for water availability, there is high likelihood of well below average water availability during late spring (Mar-Apr).
Obviously, it will vary by basin across Afghanistan.

## Slide 38: Helmand
Average to below average SWE during early spring (Jan-Feb), but well below average SWE in late spring (Mar-Apr).
Average streamflow during Mar-Apr, but well below average streamflow during the rest of the season.

## Slide 39: Argandab
Average to below average SWE during early spring (Jan-Feb), but well below average SWE in late spring (Mar-Apr).
Chances of early completion of snowmelt at least two weeks in advance.
Average streamflow during Mar-Apr, but well below average streamflow during the rest of the season.

## Slide 40: Ghazni
Average to below average SWE during early spring (Jan-Feb), but well below average SWE in late spring (Mar-Apr).
Chances of early completion of snowmelt. Given the size of the basin snowmelt could complete four to six weeks in advance.
Average streamflow during Mar-Apr, but well below average streamflow during the rest of the season.

## Slide 41: Shamal
Average to below average SWE during early spring (Jan-Feb), but well below average SWE in late spring (Mar-Apr).
Chances of early completion of snowmelt. Given the size of the basin snowmelt could complete four to six weeks in advance.
Highly variable streamflow through the season mostly because of the smaller size of the basin.

## Slide 42: Kabul-east
Average to below average SWE throughout the spring season (Jan-Apr).
Snowmelt could complete two to four weeks in advance.
Average streamflow with occasional chance of elevated flow in the river.

## Slide 43: Kokcha_Ab-i-Rustaq-lower
SWE could be highly variable over the mountainous basins in the northeast throughout the season.
Streamflow could also be highly variable and could experience flood producing flow in May-Jun.

## Slide 44: Panj
SWE could be highly variable over the mountainous basins in the northeast throughout the season.
Streamflow could also be highly variable and could experience flood producing flow in May-Jun.

## Slide 45: Khanabad-lower
SWE could be highly variable in early spring (Jan-Mar), then likely to be below average in late spring (Apr-May).
Average to below average Streamflow with occasional chance for high flow in May.

## Slide 46: Kunduz
Average to below average SWE with exceptionally above average SWE very late in the season in 2023.
Chances of early completion of snowmelt. Which could complete four to eight weeks in advance.
Average to below average Streamflow with occasional chance for high flow capable of causing floods.

## Slide 47: Khulm
Average to below average SWE with exceptionally above average SWE very late in the season in 2023.
Chances of early completion of snowmelt. Which could complete four to six weeks in advance.
Average to below average Streamflow with occasional chance for high flow capable of causing floods.

## Slide 48: Balkhab
Average to below average SWE thoughout the season.
Average to below average Streamflow with occasional chance for high flow in the river.

## Slide 49: Sari Pul
Average to below average SWE throughout the season.
Chances of early completion of snowmelt, two to four weeks in advance.
Below average Streamflow with occasional chance for moderate flow in the river.

## Slide 50: Shirin Tagab - lower
Average to below average SWE in early spring, but well below average in late spring.
Chances of early completion of snowmelt, four to six weeks in advance.
High likelihood of below average Streamflow throughout the season.

## Slide 51: Bala Murghab
Average to below average SWE in early spring, but well below average in late spring.
Chances of early completion of snowmelt, two to four weeks in advance.
High likelihood of below average Streamflow throughout the season.

## Slide 52: Hari Rod
Average to below average SWE in early spring, but well below average in late spring.
Chances of early completion of snowmelt.
High likelihood of below average Streamflow throughout the season.

## Slide 53: Farah Adraskan
Average to below average SWE in early spring, but well below average in late spring.
Chances of early completion of snowmelt, four to six weeks in advance.
High likelihood of below average Streamflow throughout the season.

## Slide 54: Observation summary
Average to below average SWE in early spring (Jan-Mar), but well below average in late spring (Apr-May).
SWE could be highly variable over the mountainous basin in the northeast.
High likelihood of early completion of snowmelt, which could be two to eight weeks in advance depending on location.
High likelihood of below average Streamflow throughout the season in southern southwestern basins.
Likelihood of average to below average streamflow in the eastern northeastern basins with occasional higher flow capable of causing floods.
Temperature would play a critical role for building up of snowpack and completion of snowmelt.

## Slide 55: Then There are Flash Flooding
However, flash flood can occur anytime and anywhere depending on the nature of the precipitation and in combination with snowmelt.
There will always be moderate likelihood of flash flooding across Afghanistan.

## Slide 56: Additional Resources
USGS Early Warning Portal: https://earlywarning.usgs.gov/
MODIS Snow Cover: https://nsidc.org/data/mod10a1f/versions/61
NASA LIS: https://lis.gsfc.nasa.gov/
NASA FLDAS: https://ldas.gsfc.nasa.gov/fldas/
FEWS NET Afghanistan: https://fews.net/middle-east-and-asia/afghanistan

## Slide 57
Thank you and let me know if you have questions.