## Slide 1
Kim Slinski (UMD/NASA), Laura Harrison (UCSB), James Verdin (UMD/NASA), Karyn Tabor (UMD/NASA), Chris Shitote (UCSB), Andrew Hoell (NOAA), Amy McNally (NASA)
Integrating Remotely Sensed data and Models to Predict Flooding in South Sudan for Humanitarian Responses
Md Shahriar Pervez & Mike Budde
U.S. Geological Survey (USGS)
Earth Resources Observation and Science (EROS) Center, Sioux Falls, SD 57198, USA.
Notes: Default title slide

## Slide 2: Famine Early Warning Systems Network (FEWS NET)
FEWS NET is a project of U.S. Dept. of State mandated to monitor & forecast food insecurity and humanitarian assistance need around the world since its inception in 1982/1983.
Near term projected outcomes through May 2026
South Sudan

## Slide 3: Famine Early Warning Systems Network
Three key components of food insecurity assessments:
  When is it happening?
  Where is it happening?
  and Who would be impacted?
FEWS NET delivers on its mandate with the help of data and analysis provided by its Science Partners

## Slide 4: Drivers of Food Insecurity
The single most important driver of food insecurity is ― Water
Either too little of water: drought
or too much of water: floods

## Slide 5: Why South Sudan?
Wetlands expanded significantly especially if one counts areas that went dry <25% of the time from near zero to 9,339 km2 since 2023.
Sudd Wetlands
Highly Food Insecure
  Combination of social and environmental factors
  Increased vulnerability due to influx of migrants fleeing conflict.
Expanding Sudd Wetlands
  Above-average precipitation 2024 + 2025 La Niña
  Shortened dry periods
  Since 2019, large volumes of water released from Lake Victoria, Uganda
  Four out of the past five years experienced devastating floods

## Slide 6: High Demand for Information in Humanitarian Response
South Sudan National Flood Preparedness & Response Task Force formed in 2024.
Local and international actors want to know the extent of inundation in advance to take preventative measures:
  Relocate refugee camps
  Evacuate in-country staff
  Assess how market access impacts food security and livelihoods
  Inform type, cost, and timing of humanitarian assistance & emergency response
International Technical Working Group formed in 2024 met bi-weekly to review data and model outputs.
  FEWS NET scientists, UN OCHA, the World Food Program, University of Reading, regional experts, non-governmental organizations
Working group consensus of flood outlooks used by Task Force, and in OCHA reports and FEWS NET Food security outlook bulletins.
https://fews.net/east-africa/south-sudan/key-message-update/november-2025/print

## Slide 7: Monitoring of flooding

## Slide 8: Satellite-based Flooded Extent (VIIRS Flood Map - VFM)
Nov : 44,098 km2
Sep : 65,480 km2
2025 inundation (yellow line) reached its annual minimum in May at a level higher than any previous year since 2012.
Inundation peaked in September.
September, October, and November 2025 VFM are much higher than average (black line), but lower than 2024 (green line).
May: 14,883 km2
Jul: 36,712 km2

## Slide 9
Satellite-based Flooded Extent (MODIS-LST)
The October 10, 2025, MODIS national flood extent is less than that of 2024. The recent flooded areas in blue shades.

## Slide 10
MODIS vs VIIRS Flood Map
Complementary to each other, both tracked the flooding well

## Slide 11
MODIS vs VIIRS Flood Map
VFM was providing improved spatial detail for flooding
Sep : 65,480 km2

## Slide 12: Landsat-based Flood Mapping
L9 false color composite 564 as RGB : Jan 08, 2024
Water pixels from Landsat Jan 08, 2024
Automated Water Extraction Index (AWEI) worked well for mapping.
Used for validation and burn area misclassification of the VFM.

## Slide 13: Seasonal Rainfall – July 6th to September 5th, 2025
During recent weeks, above-average rainfall occurred in central and southeastern South Sudan, as well as in western Ethiopia (left image).
Past 2 month (July 6th to September 5th) rainfall totals in South Sudan are average in most areas, above average in the southeast, and below average in the northeast and southwest (center). August rainfall was above average across much of central and southern South Sudan.
In Jonglei, South Sudan, especially high rainfall amounts occurred during August 10th-20th, 2025.
Past 6-pentad and past 12-pentad percent of average rainfall
Jonglei, South Sudan rainfall
Mean and 2025 pentads (CHIRPS Final, Prelim, and CHIRPS-GEFS forecast)

## Slide 14: Seasonal Rainfall – Late August to early September 2025
During the past week in South Sudan, most areas received below-average rainfall (September 1st-7th, 2025, left).
Above-average rains are forecast South Sudan this week and next week (center and right), based on the NOAA CPC outlook.
Last week rainfall anomaly
NOAA CPC Week 1 and Week 2 rainfall outlooks

## Slide 15: SWOT Satellite Altimetry - Malakal
Mid-October Nile River water levels at Malakal are above peak 2024 levels and continued to rise in late October.
End of October data are not available.
Notes:
SWOT dataset was filtered to remove data points with >0.25 m uncertainty and outliers.
Error bars represent uncertainty.

## Slide 16: Sudd Satellite Altimetry - West (008974) and East (008976) of Malakal
Data from the NASA Water Measurements Rivers and Wetlands Dataset, accessed 3 Nov 2025.
Water levels for late October 2025 are highest on record and rising.

## Slide 17: Nile River Water Levels
MWRI water levels
Juba, Mangala, Bor, Malakal, and Anakdiar remain at the Alert level.

## Slide 18: Just monitoring wasn’t good enough! There was high demand to know HOW MUCH its going to flood

## Slide 19: Forecast Challanges
Accurate forecast of natural hazards are challenging in data-poor regions like South Sudan
  Modeling complex wetlands ecosystem
  Near flat topography
  Back flow effect
  Lack of discharge information from dams upstream
  Scarce in situ datasets (weather stations) for remote sensing calibration/validation
  Very limited in situ observations of inundation extent
Sudd Wetlands: L8 true color composite

## Slide 20: Availability of Satellite-based data and Models
Precipitation
Pentadal Precipitation (CHIRPS blended station and satellite data)
Sub-seasonal forecasts (Weeks 1 and 2) (NOAA)
Monthly seasonal forecasts (North American, ECMWF, WMO)
Water Level Observations & Estimates
In Situ Streamflow Gauges MWRI gauges
Satellite Altimetry (SWOT, Hydroweb, NASA)
Hydrologic Estimates
FLDAS (FEWS NET Land Data Assimilation: runoff, streamflow)
Flooded Extent
VIIRS Flood Map (NASA VFM) from NOAA satellite imagery
MODIS Flooded extent (World Food Program)
Flood Extent Forecast
  Least Absolute Shrinkage and Selection Operator (LASSO) statistical forecasts
  INFLOW AI model (U Reading)
Since June 1st, most of South Sudan has received 300 mm to higher-than 500 mm rainfall. Seasonal totals are much higher than normal in southeastern South Sudan and southwestern Ethiopia.

## Slide 21: LASSO Forecast Model
LASSO Model Covariates:
FLDAS-Forecast Open Loop: Retrospective runoff and precipitation; by subbasin and aggregated over nested basins.
FLDAS-Forecast NMME-based Forecasts: Ensemble mean forecasts of streamflow, runoff, and precipitation; by subbasin and aggregated over nested basins.
VIIRS Inundation: By basin.
Satellite Altimetry: Water levels for Lake Victoria, Lake Albert, and Lake Kyoga.
Lead and lag months used in current LASSO model forecast. IC (Initial conditions) is the most recent month with complete observational and FLDAS-Forecast Open Loop datasets. It is also the initialization month for the FLDAS-Forecast dataset. LASSO forecasts for the months of December, January, and February not used because of burn scar contamination in the VIIRS flood mapping product.

## Slide 22: LASSO Forecast Model
LASSO-Predicted VIIRS Flood Mapping Area (km²) |  |  | 
Month | Ensemble Minimum | Ensemble Mean | Ensemble Maximum
202509 | 58,100 | 76,000 | 80,300
202510 | 68,400 | 69,200 | 69,500
202511 | 48,100 | 50,500 | 51,200

## Slide 23: INFLOW Project Forecast Model
60-day AI-based forecast of MODIS flood extent as of November 11, 2025 (red dotted line)
LASSO forecast 1-6 months with improved model skills closer to target month

## Slide 24: Knowing only flooding number wasn’t good enough! There was high demand to know WHERE those flooding would be

## Slide 25: VFM-based Flood Frequency Map
Likely areas of inundation based on monthly VFM updated every pentad (2012 to present)
Let’s assume LASSO predicted inundated area is : 11 units (each square is one unit)
+
% of times inundated out of 130 months (frequency map)
current inundated area map (initial condition)
spatial distribution of predicted inundation
Total of 12 units with initial condition
2 -> already inundated 100%, 75%
4 -> 100% cells
4 -> 95% cells
2 -> 88% cells

## Slide 26: LASSO Forecast Maps
Sep 2025 with Mid-Jul IC
72,099 km2

## Slide 27: LASSO Forecast Maps
76,092 km2
Sep 2025 with Aug IC
LASSO-Predicted VIIRS Flood Mapping Area (km²) |  |  | 
Month | Ensemble Minimum | Ensemble Mean | Ensemble Maximum
202509 | 58,100 | 76,000 | 80,300
202510 | 68,400 | 69,200 | 69,500
202511 | 48,100 | 50,500 | 51,200

## Slide 28: LASSO Forecast vs Observed
76,092 km2
Sep 2025 with Aug IC
Observed September 2025
65,480 km2
Error matrix

## Slide 29: Outcomes

## Slide 30: 2024 Outcomes
By June 2024, FEWS NET confidently forecasted that the capital Juba and its international airport would not experience the severe 1-in-60 year flooding feared by the U.S. Embassy.
In August 2024, FEWS NET dispelled concerns about a costly and disruptive evacuation of U.S. Embassy staff.
The U.S. government delivered $600 million USD in humanitarian assistance.
Assistance aimed to help increase coping capacity of estimated 65-70 percent of the population of South Sudan.
https://reliefweb.int/blogpost/scientists-get-ahead-south-sudan-floods-we-need-save-peoples-livelihoods

## Slide 31: 2025 Outcomes
OCHA estimated 1 million people affected by the 2025 floods
Enabled FEWS NET analysts to produce the earliest and most precise evidence-based assessments of severe food insecurity.
This information allows the U.S. government to determine who needs aid, where it is needed the most, and when it is needed to avert humanitarian crises.
South Sudan Task Force implemented anticipatory actions to mitigate flood impacts in the South Sudan.

## Slide 32: What’s coming in 2026
Greater chance of developing an El Niño in 2026 which tends to reduce rainfall in June-September over South Sudan
What we know now:
  consistently less flood recession in the last several years
  persistently high upstream lake and river levels
  and increased frequency of high intensity rainfall
Early expectation is “Reduced likelihood of record-breaking flooding”
South Sudan National Flood Preparedness & Response Task Force has been re-activated in April
We are sharpening our tools with more data and model improvements for the season
Two manuscripts in progress

## Slide 33: April Flood Extent
Mid-Apr 2025
VIIRS: 17,328 km2
Mid-Apr 2026
VIIRS: 14,792 km2

## Slide 34: NASA LASSO Model Forecast
The dashed yellow line represents the forecast ensemble mean.
The purple area represents the uncertainty about the forecast ensemble mean.
60,018 km2
Forecast Sept 2026 with March Initial Conditions

## Slide 35: LASSO 2026 Forecast vs 2025 Observed Inundation
60,018 km2
65,480 km2
Forecast Sept 2026 with March Initial Conditions
Observed Sept 2025

## Slide 36: Conclusion
While we live in a data-rich world, many regions are data-poor for earth observations
When faced with a real-world challenge such as a humanitarian crisis, we were able to piece together all the data we could and developed new models to meet the urgent decision-making needs
We were able to perform collaborative work internationally sharing data and knowldege for a common cause every two weeks to inform decision-making
Consensus approach for reviewing data and model outputs proved highly effective, fostering knowledge co-production, increasing collaboration, and facilitating science-to-action through a user-driven design

## Slide 37
Thank you
Questions & comments are welcome

## Slide 38: LASSO Forecast vs Observed
76,092 km2
Sep 2025 with Aug IC
Observed September 2025
65,480 km2

## Slide 39
End of May 2024
VIIRS : 11,907 km2
By the End of May 2025, there are slightly more area under water than the same in 2024.
End of May 2025
VIIRS: 14,883 km2
Initial Conditions Comparison

## Slide 40: LASSO Forecast vs Observed
Observed Oct 2025
VIIRS: 57,865 km2
66,108 km2
October 2025 Forecast

## Slide 41: SWOT Satellite Altimetry – Juba
Mid-October Nile River water levels at Juba appear to be leveling off.
Notes:
SWOT dataset was filtered to remove data points with >0.25 m uncertainty and outliers.
Error bars represent uncertainty.

## Slide 42: LASSO Model Skill Metrics
LASSO forecasts and hindcasts have been bias corrected relative to VFM observations by month and lead. Skill metrics are calculated on the bias corrected output.
Pearson correlation by lead (all ICs). |  |  |  |  | 
Lead | 1 | 2 | 3 | 4 | 5
r | 0.90 | 0.92 | 0.89 | 0.90 | 0.90
Model skill metrics for LASSO-Predicted VIIRS Flood Mapping Area for October 2025 model run. All metrics are in km². |  |  |  | 
Month | 2012-2024 Hindcast |  |  | 2025 Forecast
 | Mean Bias | RMSE | Ensemble Spread | Ensemble Spread
Nov | -200 | 5,100 | 5,400 | 1,800