## Slide 1: Flood Monitoirng and Forecast Assumptions—West Africa
FEWS NET Science Team
September 16, 2026
Notes: Default title slide

## Slide 2: Sub-seasonal Streamflow Forecast
Niger
Sokoto
Komadugu
Logone
Niger
Benue
Senegal
A
Discharges are extremely low across all major rivers in west Africa.
GloFAS Sub-seasonal forecast: Sep 14 – Oct 26, 2026
GloFAS: Sep 14 – Oct 26, 2026
@point A, on the River in northern Togo
B
C
@ point A: Niger in central Mali
@ point B: Komadugu in Nigeria
@ point C: Benue in Nigeria

## Slide 3: Seasonal Streamflow Forecast
Both NHyFAS and GloFAS models are converging for well below average flow during the peak flow season of September and October in all major Rivers in West Africa. Streamflow are expected to be at extremely low (1 to 10 percentile range), therefore, less likelihood of flooding in West Africa till the end of the season.
A
GloFAS seasonal forecast Sep 2026 – Mar 2027
B
NHyFAS seasonal forecast Sep – Jan 2027
@point B on Logone in Chad
@point A on upstream Niger in Niamey

## Slide 4: Assumption
Based on the extended streamflow forecast, the likelihood of flooding along the major Rivers in West Africa is extremely low till the end of the season. below average. However, there is a likelihood of flooding along the western coastal countries, central Mali, southern Niger, and northern Nigeria during the September-October period.