## Slide 1: 2026 Analog Year Flooding Assessment - Somalia
Shahriar Pervez
Aug 11, 2026
Notes: Default title slide

## Slide 2: Analog Years for 2026
2023, 1997, 2006 have been identified as the possible analog years for 2026 Oct-Dec season.
2023 flood extent was identified from VIIRS at 375m resolution.
1997 flood extent was identified from Landsat at 30m resolution.
There were not suitable cloud free Landsat images were available for 2006.
2015 and 2019 flood extents were identified from VIIRS at 375m resolution.

## Slide 3: Analog Year Inundation
Oct-Dec 2023
VIIRS : 12,955 km2
Oct-Dec 1997
Landsat: 4,914 km2
Note: Difference in resolution, VIIRS is at 375m and Landsat is in 30m resolution.
Source: USGS EROS

## Slide 4: Cropland and Population
ESA 2021 Cropland
UN World Population 2020
Source: USGS EROS
ESA WorldCover 2021 at 10 m resolution derived from Sentinel data.
WorldPop 2020 population data at 100 m resolution.

## Slide 5: Possible Impacts in Somalia for 2026
If flooding were to occur at 2023 level
If flooding were to occur at 1997 level
Population at risk
Cropland at risk
324,992 ha
1,029,828
157,630 ha
316,107
Area inundated
12,955 km2
4,914 km2

## Slide 6: Oct-Dec Flooding in Somalia
1997
2015
2019
Derived from Landsat 5 data
100 yr & 10 yr return period level streamflow
Area inundated: 6,052 km2
Derived from VIIRS 375 m data
2 yr & 5 yr return period level streamflow
Area inundated: 2,837 km2
Derived from 375 m data
2 yr return period level streamflow
Area inundated: 4,048 km2

## Slide 7: Possible Impacts in Somalia
If flooding were to occur at 2015 level
If flooding were to occur at 2019 level
Population at risk
Cropland at risk
160,366 ha
344,204
90,963 ha
193,319
Area inundated
4,048 km2
2,837 km2
There are more people and croplands in the Shabelle catchment than Juba.

## Slide 8
Thank you