## Slide 1: South Sudan Flood Monitoring and Prediction - 2025 Season
May 09, 2024
FEWS NET Science Team

## Slide 2: Flooding Progression
27 April 2025
VIIRS 23-27 April: 10,162 km2
08 May 2025
VIIRS 04-08 May comp: 9,859 km2
Marginal decrease in Inundation.

## Slide 3: May Initial Conditions
05 May 2024
VIIRS 01-05, 2024 : 8,738 km2
At the beginning of May 2025 has slightly more area under water than the same in 2024.
08 May 2025
VIIRS 04-08 May comp: 9,859 km2

## Slide 4: VIIRS Time Series
Inundation is currently receding, which is typical for the season.
April 2025 VIIRS inundation (yellow line) is the highest on record.

## Slide 5: Uganda Lakes Satellite Altimetry
Data from Hydroweb, accessed 9 May 2025.
Uganda Lakes remain at historically high levels, though early May2025 (yellow line), though water levels in Lake Victoria are lower than last year.

## Slide 6: Flooding in the Upper Nile State
WFP Dashboard: MODIS Temp. difference-based flooding, data from 1 – 11 of April 2025
Bands 5-4-3 (Near Infrared-R, Red-G, Green-B) Landsat from 18 of April 2025.
There appears to be some vegetation in the area that is flooded for longer than 50 days in MODIS.
Vegetation appears red with 5-4-3 color composite.

## Slide 7: Landsat Optical vs LST Signals
Landsat Land Surface Temperature (LST) in °Kelvin 18 of April 2025
Bands 5-4-3 (Near Infrared-R, Red-G, Green-B) Landsat from 18 of April 2025
That area could be with floating vegetation or very wet soil with vegetation.
Vegetation appears red with 5-4-3 color composite.

## Slide 8: Landsat Optical & Land Surface Temperature
Landsat Land Surface Temperature (LST) in °Kelvin 18 of April 2025
Bands 5-4-3 (Near Infrared-R, Red-G, Green-B) Landsat from 18 of April 2025
Difference in LST suggests, it could be more like very wet soil with vegetation.
Water
Cloud &
Burn scar
Burn scar
Water
Water
Possibly Wet soil with vegetation
Water
Cloud &
Burn scar
Burn scar
Water
Water
Possibly Wet soil with vegetation
Vegetation appears red with 5-4-3 color composite.

## Slide 9: LS vs VIIRS Inundation
Water
Cloud &
Burn scar
Burn scar
Water
Water
Possibly Wet soil with vegetation
Water
Cloud &
Burn scar
Burn scar
Water
Water
Possibly Wet soil with vegetation
Landsat-based inundation: 18 April 2025
VIIRS inundation: 23 – 27 April 2025
Landsat captured open water quite well, VIIRS also captured water relatively well. Neither VIIRS nor LS identified burn scars as water. That wet soil with vegetation area was not classified as water.

## Slide 10
Thank you