## Slide 1: South Sudan Flood Monitoring and Prediction - 2025 Season
April 30, 2024
FEWS NET Science Team

## Slide 2: Flooding Progression
6 April 2025
VIIRS 2-6 April: 11,076 km2
27 April 2025
VIIRS 23-27April comp: 10,162 km2

## Slide 3: April Initial Conditions
28 April 2024
VIIRS 24-28, 2024 : 8,995 km2
27 April 2025
VIIRS 23-27, 2025 Apr comp: 10,162 km2
Very similar flooding condition in 2025 compared to flooding in 2024 for the month of April.

## Slide 4: Flooding in the Upper Nile State
WFP Dashboard: MODIS Temp. difference-based flooding, data from 1 – 11 of April 2025
Bands 5-4-3 (Near Infrared-R, Red-G, Green-B) Landsat from 18 of April 2025.
There appears to be some vegetation in the area that is flooded for longer than 50 days in MODIS.
Vegetation appears red with 5-4-3 color composite.

## Slide 5: Landsat Optical vs LST Signals
Landsat Land Surface Temperature (LST) in °Kelvin 18 of April 2025
Bands 5-4-3 (Near Infrared-R, Red-G, Green-B) Landsat from 18 of April 2025
That area could be with floating vegetation or very wet soil with vegetation.
Vegetation appears red with 5-4-3 color composite.

## Slide 6: Landsat Optical & Land Surface Temperature
Landsat Land Surface Temperature (LST) in °Kelvin 18 of April 2025
Bands 5-4-3 (Near Infrared-R, Red-G, Green-B) Landsat from 18 of April 2025
Difference in LST suggests, it could be more like very wet soil with vegetation.
Water
Cloud &
Burn scar
Burn scar
Water
Water
Possibly Wet soil with vegetation
Water
Cloud &
Burn scar
Burn scar
Water
Water
Possibly Wet soil with vegetation
Vegetation appears red with 5-4-3 color composite.

## Slide 7: LS vs VIIRS Inundation
Water
Cloud &
Burn scar
Burn scar
Water
Water
Possibly Wet soil with vegetation
Water
Cloud &
Burn scar
Burn scar
Water
Water
Possibly Wet soil with vegetation
Landsat-based inundation: 18 April 2025
VIIRS inundation: 23 – 27 April 2025
Landsat captured open water quite well, VIIRS also captured water relatively well. Neither VIIRS nor LS identified burn scars as water. That wet soil with vegetation area was not classified as water.

## Slide 8: VIIRS vs Landsat
27 April 2025
VIIRS 23-27, 2025 Apr comp: 10,162 km2
Multiple dates in April 2025
Landsat multiple dates in April 2025: 4,709 km2
VIIRS and Landsat differ in resolution.
Landsat scenes were impacted by clouds.

## Slide 9
Thank you