## Slide 1: South Sudan Flood Monitoring and Prediction - 2025 Season
FEWS NET Science Team
September 09, 2025
Notes: Default title slide

## Slide 2: South Sudan Flooding – Key Message
Key Message:
Seasonal increase in flooded extent is well underway. The extent in 2025 is expected to be on par with 2024.
Supporting Evidence:
VIIRS Flood Mapping product analysis
Uganda lake levels are very high
Nile River water levels are on par with 2024
Above-average precipitation is expected overall for August – October
Above-average NASA LASSO model monthly inundation forecasts for September and October

## Slide 3: South Sudan Flooding – VIIRS Analysis
VIIRS Flood Mapping (VFM) product analysis
Time-series VFM monthly composites historically depict the annual minimum in May, and greatest extents in September and October.
VFM composites for 2025 indicate that the annual minimum was reached in May and that it was the highest May value in the VFM record since 2012.
VFM inundated extent effectively doubled from June to July.
Inundated area continued to expand in August. While not the highest on record, August 2025 VFM greater than flood years 2022 and 2024.

## Slide 4: VIIRS Flood Mapping (VFM) Time Series
Time-series VFM monthly composites historically depict the annual minimum in May, and greatest extents in September and October.
2025 inundation (yellow line) reached its annual minimum in May at a level higher than any previous year since 2012.
VFM inundated extent doubled from June to July.
While not the highest on record, August 2025 VFM greater than flood years 2022 and 2024.
VIIRS inundation data for 01/2012-08/2025 are from the NOAA VIIRS Flood Product and UNOSAT. Missing data: 01/2021-12/2021. Statistics are calculated using all available data.

## Slide 5: VIIRS Flood Mapping (VFM) Time Series
Time-series VFM monthly composites historically depict the annual minimum in May, and greatest extents in September and October.
2019 and later inundation has largely been greater than previous years (dark grey band).
2025 inundation (yellow line) reached its annual minimum in May at a level higher than any previous year since 2012.
VFM inundated extent doubled from June to July
While not the highest on record, August 2025 VFM greater than flood years 2022 and 2024.
VIIRS inundation data for 01/2012-08/2025 are from the NOAA VIIRS Flood Product and UNOSAT. Missing data: 01/2021-12/2021. Statistics are calculated using all available data.

## Slide 6: VIIRS Flood Mapping (VFM) Time Series - Sobet-Akobo-Pibor
VIIRS inundation data for 01/2012-08/2025 are from the NOAA VIIRS Flood Product and UNOSAT. Missing data: 01/2021-12/2021. Statistics are calculated using all available data.
VFM in the Sorbet-Akobo-Pibor basin just above the mean, but this is higher than recent years.

## Slide 7: May Initial Conditions
End of May 2024
VIIRS : 11,907 km2
By the end of May 2025 (right), there was more area under water than the same time in 2024 (left).
End of May 2025
VIIRS: 14,883 km2

## Slide 8: June Initial Conditions
End of Jun 2024
VIIRS : 18,921 km2
By the end of June, flooded areas were very much the same for 2024 and 2025.
End of Jun 2025
VIIRS: 18,704 km2

## Slide 9: July Initial Conditions
End of Jul 2024
VIIRS : 16,929 km2
End of July flooded area in 2025 is more than double compared to flooded area in 2024.
End of Jul 2025
VIIRS: 36,712 km2

## Slide 10: Flooding Progression: 5-day Composites
03 -07 Sep: 40,345 km2
04-08 May: 9,860 km2
16-20 Jul: 24,673 km2
23-27 Jul: 28,620 km2
30 Jul - 03 Aug: 24,370 km2
06-10 Aug: 23,835 km2
15-19 Aug: 26,313 km2
27-31 Aug: 42,681 km2

## Slide 11: June - July Change in Flooded Extent
End of June 2025
VIIRS : 18,704 km2
Flooded area effectively doubled from June to July in 2025.
End of July 2025
VIIRS: 36,712 km2

## Slide 12: Early August – Early Septmeber Change in Flooded Extent
Inundation almost doubled between early August and early September of 2025.
03 -07 Sep: 40,345 km2
06-10 Aug: 23,835 km2

## Slide 13: July - August Change in Flooded Extent
End of July 2025
VIIRS : 36,712 km2
Flooded area continued to increase from end of July to end of August. Relatively more inundation in the Sobet-Akobo-Pibor catchment.
End of August 2025
VIIRS: 49,631km2

## Slide 14: Expansion of Permanent Wetlands
Expansion of permanent Wetlands was determined based on successively inundated areas during the dry months of January through May in recent years (assuming the same areas were inundated during the rest of the months).
4,473 km2 since 2023
9,339 km2 inundated since 2023 for 75% of time or more
Permanent Wetlands have expanded significantly since 2023 (left),
especially if one counts areas that went dry <25% of the time (right)

## Slide 15: July - August Change in Flooded Extent
End of July 2025
VIIRS : 36,712 km2
Flooded area continued to increase from end of July to mid-August. (30-day composites)
Mid-August 2025
VIIRS: 43,688 km2

## Slide 16: End of August Flooded Extent
End of August 2024
VIIRS : 45,012 km2
End of August flooded area in 2025 (right) compared to 2024 (left). While inundation is higher nationally, less inundation is evident in 2025 in Warrap state, west of the Sudd wetlands.
End of August 2025
VIIRS: 49,361 km2

## Slide 17: Flooding Progression: 5-day Composites
30 Jul-03 Aug: 24,370 km2
04-08 May: 9,860 km2
18-22 Jun: 11,100 km2
25-29 Jun: 13,870 km2
3-7 Jul: 14,370 km2
9-13 Jul: 14,620 km2
16-20 Jul: 24,673 km2
23-27 Jul: 28,620 km2

## Slide 18: Comparison with FloodBase
FloodBase: July 2025
19,727 km2
Note the difference in resolution: FloodBase is at 12-m and VIIRS is at 375-m
Recall that VIIRS mapping includes all pixels classified to be 41% or more as flooded
VIIRS: July 2025
VIIRS: 36,712 km2

## Slide 19: Flooding Progression
30 Jul-03 Aug: 24,370 km2
11-15 Jun: 11,360 km2
18-22 Jun: 11,100 km2
25-29 Jun: 13,870 km2
3-7 Jul: 14,370 km2
9-13 Jul: 14,620 km2
16-20 Jul: 24,673 km2
23-27 Jul: 28,620 km2

## Slide 20: South Sudan Flooding – Uganda Lakes
Uganda lake levels are very high
Lake Victoria and Lake Kyoga are below that of 2024, but still very high, just above the historical 90th percentile rank.
Lake Albert water levels are above the historical 90th percentile rank and are comparable to that of 2024.
High lake levels imply high River Nile flows from Uganda to South Sudan, a principal source of water for the annual expansion of the Sudd wetland.

## Slide 21: Uganda Lakes Satellite Altimetry
Data from Hydroweb, accessed 7 Sept. 2025.
2025 Lake Victoria and Lake Kyoga (yellow line) are just above the historical 90th percentile rank.
2025 Lake Albert levels (yellow line) are above the historical 90th percentile rank and are comparable to 2024 (green line).
High lake levels imply high White Nile flows from Uganda to South Sudan, a principal source of water for the annual expansion of the Sudd wetland.

## Slide 22: South Sudan Flooding – Nile River Water Levels
Nile River water levels are comparable to 2024 and are rising
MWRI water level data show Mangala at High level, and Bor and Malakal at Alert level.
Sudd water levels from satellite altimetry are above the 90th percentile.
Time-series Surface Water and Ocean Topography (SWOT) data at Nimule indicate that the Nile River water levels are comparable to early September 2024.
Juba, Malakal, and New Fangak Nile River water levels are above early September 2024. Downstream water levels (Malakal and New Fangak) are comparable to peak 2024 levels.

## Slide 23: Nile River Water Levels
MWRI water levels
Mangala is at very close to 10-yr return period level (High)
Juba is at close to Alert level
Malakal, Bor and Anakdiar are at Alert level.

## Slide 24: Sudd Satellite Altimetry
Data from the NASA Water Measurements Rivers and Wetlands Dataset, accessed 7 Sept. 2025.
Sudd1 water levels (located north of Bor) are above the 90th percentile, higher than 2024, and rising.
Sudd2 water levels (located south of Adok) are above the 90th percentile, comparable to 2024, and rising.

## Slide 25: SWOT Satellite Altimetry – Nimule
Mid-August Nile River water levels upstream are rising.
Notes:
SWOT dataset was filtered to remove data points with >0.25 m uncertainty and outliers.
Error bars represent uncertainty.
Data citation: Frank Greguska, Nikki Tebaldi, Victoria McDonald, Vanesa, & Cassie Nickles. (2024). podaac/hydrocron: 1.3.0a5 (1.3.0a5). Zenodo. https://doi.org/10.5281/zenodo.11193245, accessed 8 Sept 2025.

## Slide 26: SWOT Satellite Altimetry – Juba
Nile River water levels at Juba are above 2024 and rising.
Notes:
SWOT dataset was filtered to remove data points with >0.25 m uncertainty and outliers.
Error bars represent uncertainty.
Data citation: Frank Greguska, Nikki Tebaldi, Victoria McDonald, Vanesa, & Cassie Nickles. (2024). podaac/hydrocron: 1.3.0a5 (1.3.0a5). Zenodo. https://doi.org/10.5281/zenodo.11193245, accessed 8 Sept 2025.

## Slide 27: SWOT Satellite Altimetry - Malakal
Nile River water levels at Malakal are just under peak 2024 levels and are rising.
Notes:
SWOT dataset was filtered to remove data points with >0.25 m uncertainty and outliers.
Error bars represent uncertainty.
Data citation: Frank Greguska, Nikki Tebaldi, Victoria McDonald, Vanesa, & Cassie Nickles. (2024). podaac/hydrocron: 1.3.0a5 (1.3.0a5). Zenodo. https://doi.org/10.5281/zenodo.11193245, accessed 8 Sept 2025.

## Slide 28: SWOT Satellite Altimetry - New Fangak
Nile River water levels at New Fangak are just under peak 2024 levels and are rising.
Notes:
SWOT dataset was filtered to remove data points with >0.25 m uncertainty and outliers.
Error bars represent uncertainty.
Data citation: Frank Greguska, Nikki Tebaldi, Victoria McDonald, Vanesa, & Cassie Nickles. (2024). podaac/hydrocron: 1.3.0a5 (1.3.0a5). Zenodo. https://doi.org/10.5281/zenodo.11193245, accessed 8 Sept 2025.

## Slide 29: South Sudan Flooding – Precipitation Forecasts
Mainly average to above-average rainfall occurred during recent weeks, with above-average amounts in August in central and southeastern South Sudan and in western Ethiopia.
Past 2-month totals, from early July to early September, are mainly average with above-average totals in parts of central and southeastern South Sudan and southwestern Ethiopia.
During September, rainfall was below average during the first week and will likely be above-average during the next two weeks.
Above-average September-November 2025 rainfall totals are forecast by ECMWF and NMME models (September initial conditions)
Should these forecasts verify, above-average rainfall and runoff will significantly increase flooding.

## Slide 30: Seasonal Rainfall – July 6th to September 5th, 2025
During recent weeks, above-average rainfall occurred in central and southeastern South Sudan, as well as in western Ethiopia (left image).
Past 2 month (July 6th to September 5th) rainfall totals in South Sudan are average in most areas, above average in the southeast, and below average in the northeast and southwest (center). August rainfall was above average across much of central and southern South Sudan.
In Jonglei, South Sudan, especially high rainfall amounts occurred during August 10th-20th, 2025.
Past 6-pentad and past 12-pentad percent of average rainfall
Jonglei, South Sudan rainfall
Mean and 2025 pentads (CHIRPS Final, Prelim, and CHIRPS-GEFS forecast)

## Slide 31: Seasonal Rainfall – Late August to early September 2025
During the past week in South Sudan, most areas received below-average rainfall (September 1st-7th, 2025, left).
Above-average rains are forecast South Sudan this week and next week (center and right), based on the NOAA CPC outlook.
Last week rainfall anomaly
NOAA CPC Week 1 and Week 2 rainfall outlooks

## Slide 32: Seasonal Rainfall – September - November 2025
Above-average rainfall is forecast for September and October 2025, according to an ensemble forecast that uses ECMWF and NMME model forecasts released in early September. Source: UCSB CHC.
ECMWF and NMME ensemble forecast for SON 2025 rainfall (September initial conditions)

## Slide 33: South Sudan Flooding – LASSO Forecasts
NASA LASSO Model Monthly Inundation Forecasts
The LASSO model forecasts VIIRS Flood Mapping (VFM) monthly inundation extents based on recent and forecast precipitation, runoff, and Uganda lake levels.
Using inputs available in August 2025, the LASSO model forecasts VFM extents in September to be lower than September 2024 and extents in October 2025 that are comparable to 2024.

## Slide 34: LASSO Inundation Forecasts – September 2025
Using inputs available in August 2025:
The maximum inundation forecasted is for October 2025.
The ensemble mean LASSO forecast for September 2025 is lower than September 2024, but there is considerable ensemble spread.
The ensemble mean LASSO forecast for October 2025 VFM is comparable to October 2024.
VIIRS inundation data for 01/2012-08/2025 are from the NOAA VIIRS Flood Product and UNOSAT. Missing data: 01/2021-12/2021. Statistics are calculated using all available data.
LASSO-Predicted VIIRS Flood Mapping Area (km²) |  |  | 
Month | Ensemble Minimum | Ensemble Mean | Ensemble Maximum
202509 | 54,800 | 65,000 | 75,000
202510 | 65,600 | 67,600 | 69,000
202511 | 45,600 | 47,900 | 50,100

## Slide 35: LASSO Inundation Forecasts
VIIRS inundation data for 01/2012-08/2025 are from the NOAA VIIRS Flood Product and UNOSAT. Missing data: 01/2021-12/2021. Statistics are calculated using all available data.
July IC 2025
August 2025 IC - Early
Actual August 2025 inundation and LASSO-Early forecasted September 2025 inundation (left) are lower than the LASSO forecasts from the July 2025 ICs (right).
October and November 2025 forecasts for each model are comparable.

## Slide 36: LASSO Inundation Forecasts – Comparison with Early Model
August 2025 IC
August 2025 IC - Early

## Slide 37: LASSO Forecast Maps
Oct 2025 with Aug IC Early
64,961 km2
67,793 km2
Sep 2025 with Aug IC Early

## Slide 38: LASSO Forecast Maps
Oct 2025 with Aug IC
76,092 km2
69,197 km2
Sep 2025 with Aug IC

## Slide 39: LASSO Model - Early Model
LASSO Model Covariates:
FLDAS-Forecast Open Loop: Retrospective runoff and precipitation; by subbasin and aggregated over nested basins.
FLDAS-Forecast NMME-based Forecasts: Ensemble mean forecasts of streamflow, runoff, and precipitation; by subbasin and aggregated over nested basins.
VIIRS Inundation: By basin.
Satellite Altimetry: Water levels for Lake Victoria, Lake Albert, and Lake Kyoga.
Lead and lag months used in current LASSO model forecast. IC (Initial conditions) is the most recent month with complete observational and FLDAS-Forecast Open Loop datasets. It is also the initialization month for the FLDAS-Forecast dataset. LASSO forecasts for the months of December, January, and February not used because of burn scar contamination in the VIIRS flood mapping product.
 | Lag 3 | Lag 2 | Lag 1 | IC | Lead 1 | Lead 2 | Lead 3 | Lead 4 | Lead 5
 | May 25 | Jun 25 | Jul 25 | Aug 25 | Sep 25 | Oct 25 | Nov 25 | Dec 25 | Jan 26
FLDAS Open Loop | X | X | X |  |  |  |  |  | 
FLDAS Forecast |  |  |  | X | X | X | X | X | X
VIIRS |  |  |  | X |  |  |  |  | 
Altimetry | X | X | X | X |  |  |  |  | 
LASSO Forecast |  |  |  |  | X | X | X | X | X

## Slide 40: LASSO Model Skill Metrics
LASSO forecasts and hindcasts have been bias corrected relative to VFM observations by month and lead. Skill metrics are calculated on the bias corrected output.
Pearson correlation by lead (all ICs). |  |  |  |  | 
Lead | 1 | 2 | 3 | 4 | 5
r | 0.90 | 0.91 | 0.89 | 0.90 | 0.90
Model skill metrics for LASSO-Predicted VIIRS Flood Mapping Area for August 2025 initial conditions. All metrics are in km². |  |  |  | 
Month | 2012-2024 Hindcast |  |  | 2025 Forecast
 | Mean Bias | RMSE | Ensemble Spread | Ensemble Spread
Sep | -3,300 | 8,800 | 5,100 | 20,200
Oct | -1,900 | 13,400 | 6,000 | 3,400
Nov | -1,700 | 6,400 | 3,700 | 4,500

## Slide 41
Thank you