## Slide 1: South Sudan Flood Monitoring and Prediction - 2024 Season
July 11, 2024
FEWS NET Science Team

## Slide 2: Prime Question
What is the expected/predicted map(s) of inundation over South Sudan during the upcoming rainfall season of 2024?

## Slide 3: Data

## Slide 4: Flood Mapping from VIIRS
Sobet
Akobo
Pibor
Example: NOAA VIIRS 5-day comp.: 26 – 30 Jun 2024
(% of the pixel)
VIIRS Data
375 m x 375 m pixels
Maps % of the pixel inundated
It’s a 5-day composite
VIIRS data available since 2012 with a few missing periods.
Method
6 composites (5th, 10th, 15th, 20th, 25th, and 30th) were used to create monthly composite.
Only pixels with 41 – 100% inundated were considered.
Isolated inundated areas less than 0.43 Km2 were removed in a clean up process.

## Slide 5: Nile Catchments and Available Data
FLDAS streamflow (retrospective & forecast)
FLDAS total runoff (retrospective & forecast)
CHIRPS rainfall
Lake Victoria and Lake Albert Altimetry water level
Bias-corrected spatially downscaled NMME precipitation forecast
FLDAS and CHIRPS data are available since 1981 and water level data since 1992

## Slide 6: Lag Analyses

## Slide 7: Inundated Areas
Inundated areas by month
No data for 2021

## Slide 8: Lag Correlation at National Level
at 3-month lag over the entire region
But can be at 1&2-month lag for SAP and upper White Nile basins.
at 1-month lag over the entire region
+ for MN, UWN and *SAP basins.
No reasonable correlation over the entire basin
but
at 0-month lag for SAP discharge
at 3-month lag
Rainfall
Runoff
Streamflow
LV Water Level
0
1
2
3
Lag (months)
Variables
Sub-catchments
SAP – Sobet-Akobo-Pibor
MN – Mountain Nile
UWN – Upper White Nile

## Slide 9: Lag Correlation
National inundated area vs SAP Rainfall, Runoff and Streamflow
Additional evidence how complex the flooding is in the Sudd Wetlands
It suggests contribution of cross-boundary flow for flooding

## Slide 10: Inundation Prediction

## Slide 11: LASSO Regression
LASSO: Least Absolute Shrinkage and Selection Operator
Regression analysis method that performs both variable selection and regularization in order to enhance the prediction accuracy and interpretability of the resulting statistical model.
The lasso method assumes that the coefficients of the linear model are sparse, meaning that few of them are non-zero.
https://en.wikipedia.org/wiki/Lasso_(statistics)
Method Citation: Santosa, F., & Symes, W. W. (1986). Linear Inversion of Band-Limited Reflection Seismograms. SIAM Journal on Scientific and Statistical Computing, 7(4), 1307–1330. https://doi.org/10.1137/0907087

## Slide 12: LASSO Regression
Advantages:
Uses a penalty function (regularization) to produce a parsimonious data model, reducing overfitting.
Covariates do not need to be independent.
Not a “black box”, method estimates coefficients for each covariate so you can see how imporant each retained covariate is in the data model.
Disadvantages:
Assumes a linear model, i.e., can not represent nonlinearities.
Will only select one (or a few) covariates from a set of correlated predictors and shrinks the rest to zero.
This selection can be somewhat arbitrary, and often changes each time you fit the model, so you cannot estimate confidence intervals for the coefficients.

## Slide 13: LASSO Regression
LASSO Model Covariates:
FLDAS-Forecast Open Loop: Lag 0 – Lag 3 runoff and precipitation, aggregated over nested basins and separately by subbasin.
FLDAS-Forecast NMME Forecasts: 1-6 month ensemble mean forecasts of streamflow, runoff, and precipitation, aggregated over nested basins and separately by subbasin.
Lag 0 VIIRS inundation
Lake Victoria and Lake Albert altimetry
Predicted Variables:
Leads 1-6 inundation

## Slide 14: Coefficients for LASSO Models
Primary drivers of the Lead 1 model:
VIIRS inundation
Current lead runoff forecast for White Nile basin
Lake Victoria altimetry
Previous lag precipitation for the Albert Nile, Sobet-Akobo-Pibor, and Mountain Nile basins
Notes:
Coefficients shown for the LASSO model predicting the maximum inundation (i.e., the highest of 20 ensemble predictions for the indicated lead).
Lag 0 = April 2024, Lag 1 = March 2024, …
Lead 1 = May 2024 forecast, Lead 2 = June 2024 forecast, …
10 largest coefficients for covariates for Lead 1 National LASSO model

## Slide 15: Coefficients for LASSO Models
Primary drivers of the Lead 5 and 6 models:
Lake Victoria and Lake Albert altimetry
Previous lead/lag precipitation and runoff for the White Nile, Albert Nile, Victoria Nile, and Mountain Nile basins
Current lead runoff forecast for White Nile and Mountain Nile basins
10 largest coefficients for covariates for Lead 5 and 6 National LASSO models

## Slide 16: LASSO Model Predictions for May-Oct 2024
LASSO was run 20 times to generate an ensemble prediction of national level inundation percentile

## Slide 17: Predicted Inundation Mapping

## Slide 18: LASSO Estimates for 2024
Predicted inundated areas with May initial condition.
Predicted inundated percentiles were converted to inundated areas.

## Slide 19: Predicted Estimate to Spatial Distribution
82
82
82
82
100
45
45
100
100
100
100
95
95
95
95
88
88
87
87
65
65
65
65
73
73
75
73
32
25
C
C
P
P
P
P
P
P
P
P
P
P
P
P
Let’s say LASSO predicted inundated area is : 9 units (each square is one unit)
% of times inundated out of 130 months (frequency map)
current inundated area map (initial condition)
spatial distribution of predicted inundation
Total of 12 units with initial condition
+

## Slide 20: Flood Frequency Maps
All available months (133 months)
JASOND months (65 months)
Seasonal (JASOND) frequency map was used in mapping predicted inundation for Sep and Oct of 2024

## Slide 21: Flood Frequency Maps
Updated (ASO of 2022) JASOND months (68 months)
JASOND months (65 months)
Seasonal (JASOND) frequency map was used in mapping predicted inundation for Sep and Oct of 2024

## Slide 22: Initial Inundation Map
Initial Condition (IC): MAY 2024

## Slide 23: Predicted Inundation Map
63,330 km2
Sep 2024 with May IC
Oct 2024 with May IC
63,330 km2
Notes: Because of the insignificant difference (only 51 km2) in LASSO predicted estimates for Sep and Oct, the mapped areas are the same for 2024.

## Slide 24: Rainfall & Discharge Analog Year
2020
2016
2017
2014
Discharge at jinja dam
Starting in May 2024: 2,400 m3s-1
Starting in May 2020: 2,200 m3s-1
Flooding at equal magnitude or more than the flooding in 2020 expected – Ministry of Water Resources & Irrigation, South Sudan.
NMME ensemble mean for June 2024: 104 mm
Analog Year
2020 was identified as the analog year based on rainfall and discharge
2020 Sep inundation: 58,820 Km2
2020 Oct inundation: 61,663 Km2

## Slide 25: Analog Based Inundation Map
63,330 km2
Sep 2024 with May IC
Oct 2024 with May IC
70,805 km2

## Slide 26: Initial Conditions Comparison
11,931 km2
May 2024 IC
May 2020 IC
9,404 km2
May 2022 IC
10,998 km2

## Slide 27: Comparison with 2020
Sep 2020
Sep 2024 with May IC
Sep 2024 with May IC
Observed: 58,820 km2
63,330 km2
Based on LASSO model
63,330 km2
Based on analog year

## Slide 28: Comparison with 2020
Oct 2020
Oct 2024 with May IC
Oct 2024 with May IC
Observed: 61,664 km2
63,330 km2
Based on LASSO model
70,805 km2
Based on analog year

## Slide 29: Comparison with 2022
Sep 2022
Sep 2024 with May IC
Sep 2024 with May IC
Observed: 29,805 km2
63,330 km2
Based on LASSO model
63,330 km2
Based on analog year

## Slide 30: Comparison with 2022
Oct 2022
Oct 2024 with May IC
Oct 2024 with May IC
Observed: 68,449 km2
63,330 km2
Based on LASSO model
70,805 km2
Based on analog year
Note the difference in predicted vs observed maps over northeastern South Sudan.

## Slide 31: Sources of Difference
Streamflow was higher in 2020 than it was in 2022, but inundation was higher in 2022 in White Nile subbasin.
Riverine flow wasn’t helpful explaining the high level of inundation in 2022.
observed
forecast

## Slide 32: Sources of Difference
Precipitation was higher in 2022 than 2020 in White Nile subbasin.
It is expected to be even higher than 2022 in Sep and Oct of 2024.
observed
forecast

## Slide 33: Sources of Difference
Runoff was higher in 2022 than 2020 in White Nile subbasin.
It is expected to be even higher than 2022 in Sep and Oct of 2024.
High inundate area could have contributed by overland flow than riverine flow in 2022.
observed
forecast

## Slide 34: Comparison with 2022
Oct 2022
Oct 2024 with May IC
Oct 2024 with May IC
Observed: 68,449 km2
63,330 km2
Based on LASSO model
70,805 km2
Based on analog year
Based on the forecast precipitation and runoff, more areas could be flooded in the White Nile catchment in the northeastern South Sudan than it is shown on the October predicted flood maps.

## Slide 35: Impact Assessment
Cropland vulnerable to flooding in October of 2024: ~10,790 hectares
Out of total 289,364 hectares (entire country)
~828,000 people are vulnerable to flooding in October of 2024.
Out of 11.2 million
Not including displaced people moving in from Sudan

## Slide 36
Thank you

## Slide 37: Coefficients for LASSO Models
10 largest coefficients for covariates for Lead 2 and Lead 3 National LASSO models
Notes:
Coefficients shown for the LASSO model predicting the maximum inundation (i.e., the highest of 20 ensemble predictions for the indicated lead).
Lag 0 = April 2024, Lag 1 = March 2024, …
Lead 1 = May 2024 forecast, Lead 2 = June 2024 forecast, …

## Slide 38: Coefficients for LASSO Models
10 largest coefficients for covariates for Lead 4 and Lead 6 National LASSO models
Notes:
Coefficients shown for the LASSO model predicting the maximum inundation (i.e., the highest of 20 ensemble predictions for the indicated lead).
Lag 0 = April 2024, Lag 1 = March 2024, …
Lead 1 = May 2024 forecast, Lead 2 = June 2024 forecast, …