## Slide 1: South Sudan Flood Monitoring and Prediction - 2024 Season
October 09, 2024
FEWS NET Science Team

## Slide 2: Surface Water Extent Mapping from Landsat
36 Landsat scenes required to cover South Sudan.
Jan – Apr period is relatively cloud free.
We mapped surface water extent from Landsat using AWEI algorithm (Feyisa et al., 2014).
Mapping was done for 2023 and 2024 Jan to Apr.
Roughly 60-70 Landsat scenes were used to create a monthly surface water extent composite.

## Slide 3: Surface Water Extent Comparison
Big difference in inundated areas from Landsat and VIIRS for January of 2024.
Inundation from Landsat, January 2024: 9,571 km2
Inundation from VIIRS January 2024: 74,925 km2

## Slide 4: Surface Water Extent Comparison
L9 false color composite 564 as RGB : Jan 08, 2024
Water pixels from Landsat Jan 08, 2024
Water pixels from VIIRS Jan 2024
This comparison of Landsat image, Landsat derived water pixels, and VIIRS water pixels shows how VIIRS was over estimating water pixels by including bare ground, perhaps with wet soil after the flood water retreated in January of 2024.
Similar overestimation in VIIRS were also observed in Feb, Mar and Apr.

## Slide 5: L9 false color composite 564 as RGB
Another example of over estimation of inundation in VIIRS by classifying flood residuals as flooded, where as AWEI was identifying visible water areas only.
L9 false color composite 654 as RGB
Inundation from Landsat, February 2024
L9 false color composite 654 as RGB
Inundation from VIIRS February 2024

## Slide 6: Inundation in South Sudan
No more double peak in the inundated areas in South Sudan.
Most likely high inundated area numbers for Jan – Apr for other years from VIIRS were results of overestimation.
Inundated area from VIIRS all months
Jan-Apr inundated area from Landsat, rest of the months from VIIRS

## Slide 7
Thank you