## Slide 2: SRTM
NGA SRTM void filled
  90 meter released
  30 meter released
SRTM Plus (version 3) (2013)
  90 meter released
  30 meter released
PlanetDEM (SRTM v4? source)
  90 meter released
NASADEM (reprocess SRTM source)
  30 meter release date 2017

## Slide 3: NASADEM
Coverage/cell size/availability
  Global/1-arcsecond (30 meters)/release estimated 2017
Accuracy
Source data
  NASA SRTM Digital Elevation Model Data at full resolution
  NASA ICESat/Geoscience Laser Altimeter (GLAS) surface elevation measurements
  ASTER Global DEM (GDEM) version 2.0
  National Elevation Dataset (NED) for US and Mexico produced by USGS
  USGS GMTED2010 developed by USGS and NGA
  Canadian Digital Elevation Data produced by Natural Resources Canada
Costs
  none
Use/distribution restrictions
  30-meter data will be distributable
Citations
  NASA, n.d., NASADEM: Creating a New NASA Digital Elevation Model and Associated Products, available at https://earthdata.nasa.gov/our-community/community-data-system-programs/measures-projects/nasadem-nasa-digital-elevation-model

## Slide 12: TanDEM-X/TerraSAR WorldDEM
Coverage/cell size/available
  Global/12 meters/released in part
Accuracy
  Vertical error (LE90): 10 m absolute; relative (< 20% 2m; >20% 4m)
  Horizontal error (CE90): 10 m absolute
Source data
  TanDEM-X
  TerraSAR
Costs
  Science TanDEM-X DEM – 0.4 arc-second (12m); 1 arc-second (30m); 3 arc-second (90m)
  Commercial WorldDEM - 0.4 arc-second (12m)
Use/distribution restrictions
  Restricted use product, which cannot be transferred or disclosed
Citations
  TanDEM-X DEM Product Specification available at https://tandemx-science.dlr.de
  WorldDEM available at http://www.astrium-geo.com/worlddem/

## Slide 13: SPOT Elevation30
Coverage/cell size/available
  global/1-arcseconds (30 meters)/released in part
Accuracy
  Vertical error (LE90): 10-30m
  Horizontal error (CE90): 10-16m
Source data
  SPOT 5 HRS
  SRTM DEM fill
Costs
  Commercial product
Use/distribution restrictions
  Restricted use product, which cannot be transferred or disclosed
Citations
  Elevation30 Technical Information, available at http://www.astrium-geo.com/en/198-elevation30
  Astrium, 2005, SPOT DEM Product Description Version 1.2, available at http://www2.astrium-geo.com/files/pmedia/public/r467_9_spot_dem_product_description.pdf
  Astrium, 2006, SPOT DEM Precision Product Description Version 1.0, available at http://www2.astrium-geo.com/files/pmedia/public/r468_9_spot_dem_precision_product_description.pdf
  Astrium, 2011, Reference3D Product Description Version 6.1, available at http://www2.astrium-geo.com/files/pmedia/public/r469_9_reference3d_product_description_201105.pdf

## Slide 14: ALOS World 3D
Coverage/cell size/available
  global/1-arcseconds/30 meters/after March 2016
Accuracy
  Vertical accuracy: 5m
  Horizontal precision: 5m
Source data
  ALOS-2 PRISM
Costs
  30-meter product free of charge
Use/distribution restrictions
  unknown
Citations
  Precise Global Digital 3D Map "ALOS World 3D" Homepage, 2014, available at http://www.eorc.jaxa.jp/ALOS/en/aw3d/index_e.htm