## Slide 1: Enhanced Flood Monitoring and Forecasting
Md Shahriar Pervez, Michael Budde, & James Rowland
spervez@usgs.gov Tel: 605.594.6838
January 22, 2024

## Slide 2: Outline
General Terminologies
Return Period
  Discharge
  Maps
Monitoring Floods
  Data sources and processing
  Validation
  Observed data
  Streamflow monitoring system
Forecasting Floods
  Data sources

## Slide 3: General Terminologies

## Slide 4: Flood Terms
Riverine flood - A riverine flood is any relatively high streamflow that overtops the natural or artificial banks of a river causing partial or complete inundation of typically dry lands.
Flash flood – A rapid flow of high water caused by excessive rainfall or in combination with snowmelt in a short period of time.
Streamflow - The water moving across the Earth’s surface in streams.
Discharge - Discharge is the measured volume of water that moves past a cross section in the river in a given amount of time. It is usually expressed in m3s-1 or ft3s-1.
River water level - It is the height of the water in the river, measured relative to an arbitrary fixed point. It is also known as river stage.

## Slide 5: Flood Terms
Floodplain - The floodplain is the relatively flat lowland that borders a river, usually dry but subject to flooding. Floodplain soils are former flood deposits.
Hydrograph - A hydrograph is a graph that shows changes in discharge or river stage over time. The time scale may be in minutes, hours, days, months, years, or decades.
Bankfull - The water level at which the rising water completely fills the stream or river, and any further rise would result in water moving into the flood plain.
Flood risk – It is the river water level at which some type of physical or economical hardship occurs along a river.
Runoff - The excess water that no longer infiltrates into the soil but instead moves on the Earth’s surface or sub-surface toward streams.

## Slide 6: Return Period

## Slide 7: Definition
Flood Return Period - The average number of years between floods of a certain size is the recurrence interval or return period. The actual number of years between floods of any given size varies a lot because of the naturally changing climate.
Typically return periods are calculated from observed data.
For example – out of 15 years of observed flooding data, there should be at least 3 events of 5-year return period flooding.
Yes, a 5-year flood can happen 2 years in a row, and the third one could be 5- or 10-years latter.
A 5-year flood also expressed as 1 in 5-year return period flood has a 1/5 = 0.2 or 20% chance of being exceeded in any one year.

## Slide 8: How are They Calculated?
They are calculated from peak annual discharge or river stage

## Slide 9: How are They Calculated?
The 3-year return period discharge for each monitoring section of the river in Afghanistan.

## Slide 10: Flood Return Period Maps
35-yr return period
2-yr return period
5-yr return period
10-yr return period
20-yr return period
Sep 2022 VIIRS
FloodBase return period maps for a section of the Niger River in Nigeria based on Landsat flood maps

## Slide 11: Flood Return Period Maps
FloodBase 20-yr return period map
FloodBase September 2022
FloodBase 35-yr return period map
Inundated area
24,450 km2
Inundated area
32,852 km2
Inundated area
18,528 km2
Sokoto
Komadugu
Benue
Niger
While total area wise 2022 flood did not exceed 20-yr return period area yet, but along major rivers (Niger, Benue and Komodugu) it exceeded extent of a 20-yr return period flood.

## Slide 12: JRC Flood Return Period Global Maps
10-year return period
50-year return period
% pixel area
% pixel area
Differences are in fractional inundation per pixel – difficult to utilize.

## Slide 13: Flood Monitoring – data sources and processing

## Slide 14: VIIRS Composited Flood Product
The VIIRS Composited Flood Products are used to filter out cloud cover through a maximal water-fraction composition process and thus derive the maximal flood extent during a flood event from the VIIRS NRT flood maps of Suomi-NPP and NOAA-20.
The routinely global VIIRS Composited Flood Products include daily composited flood product and 5-day composited flood product.
The composition process is done by dividing the global land into 136 AOIs.
(% of the pixel)
VIIRS 5-day composite.: 22 – 26 Nov 2023

## Slide 15: VIIRS Coverage in 136 AOIs
The global land is divided into 136 AOIs for the VIIRS composition process and data archive
The composited products are available at this link: https://www.ssec.wisc.edu/flood-map-demo/ftp-link/ftp-link-VIIRS5day/
Historical data are available here: https://noaa-jpss.s3.amazonaws.com/index.html#JPSS_Blended_Products/VFM_5day_GLB/ShapeZIP/

## Slide 16: Potentail Issues
Agricultural-related flooding: Some flooding water shown in the VIIRS flood maps may not be any hazard-related flooding, but from agriculture-related activities such as rice paddy planting and aquaculture.
Tides and Marsh lands: In some regions especially coastal areas, consistent flooding may be detected in the flood maps. These floods are mostly caused by the tides or occur over marsh lands, which do not pose any social impact.
Water reference map: The current water reference map we use for global flood mapping is from global water bodies of ESA CCI and MODIS global water mask (MOD44W Version 006). It might not reflect the new reservoirs and other hydraulic projects built after 2015, which may take some normal water as flooding water.
Solar Eclipses: For granules that are flagged as an “eclipse”, the flood product will not be produced.
(% of the pixel)
VIIRS 5-day composite.: 31 Aug – 04 Sep 2023
Nile
Blue Nile

## Slide 17: VIIRS Flood Risk Map for Weekly Hazards
VIIRS 5-day composite.: 11 – 15 Jan 2024
(% of the pixel)
Flood risk polygons for 18-24 Jan 2024 Outlook

## Slide 18: VIIRS Flood Map for Other Assessments
2023 Oct-Dec analog year flooding in South Sudan
2015
2019
Sudan area inundated: 9,266 km2
South Sudan area inundated: 39,299 km2
Sudan area inundated: 21,055 km2
South Sudan area inundated: 62,487 km2

## Slide 19: VIIRS Flood Map for Other Assessments
2023 Oct-Dec analog year flooding in Somalia
2015
2019
Area inundated: 2,837 km2
Area inundated: 4,048 km2
Oct-Nov 2023

## Slide 20: Flooding Impacts in Malawi
NOAA VIIRS 5-day comp.: 16 – 20 Mar 2023
(% of the pixel)
Inundated areas overlaid on ESA cropland
Impacted cropland by district

## Slide 21: Flooding Across Africa
Flooding in 2022 (Jun – Dec)
Flooding in 2023 (Jun – Dec)

## Slide 22: Mapping Floods from Other Sources of Data
Oct-Dec 1997 Flooding from Landsat using AWEI (Automated Water Extraction Index) Feyisa et. al., 2014 method
Landsat LST June 01, 2021 (South Sudan)

## Slide 23: Validation of the VIIRS Flood Maps
September 2022
VIIRS at 375 m resolution
September 2022
FloodBase map at 10 m resolution

## Slide 24: Validation of the VIIRS Flood Maps
Oct-Nov 2023
VIIRS at 375 m resolution
Oct-Nov 2023
FloodBase map at 10 m resolution

## Slide 25: FloodBase Coverage
Months of mapping: July, August, September, October and November
During La Nina Years
During El Nino Years

## Slide 26: SWALIM Observed Water Level Data
Belet weyne
Luuq
Bualle
Bardheere
Dollow
Bulo Burti
Jowhar
Gage Location: RED – at bankfull
SWALIM Observed Water Level: 27 Nov 2023
Entire Juba River at bankfull with increasing magnitude at Bardheere and downstream.
Shabelle at bankfull in Belet weyne and Bulo Burti (2 out of 3 locations) and at moderate risk of flooding near Jowhar.

## Slide 27: Afghanistan Streamflow Monitoring
In collaboration with NASA, a complete streamflow monitoring system has been developed and run operationally.

## Slide 28: Flood Forecasting – models and data sources

## Slide 29: GEOGloWS Streamflow Forecast
GEOGloWS Forecast.: 26 Nov – 12 Dec 2023
GEOGloWS Forecast.: 26 Nov – 12 Dec 2023
@ point A: combine flow of Lagh Dera and Lagh Jura
@ point B: on Juba River near outlet
B
A
Juba discharges near the outlet are expected to be at 10-year return period level for the next few days.

## Slide 30: GloFAS Streamflow Forecast
2-yr 5-yr 20-yr
Ethiopia
Somalia
GloFAS streamflow forecast: (12 Nov – 12 Dec 2023)
High likelihood of Juba discharge in Ethiopia and Somalia to be at 5-yr to 20-yr return period level until late November.

## Slide 31: Seasonal Streamflow Forecast
GloFAS seasonal forecast Jan - Apr 2024
NHyFAS monthly forecast Jan - May 2024
Streamflow for Zambezi including its tributaries are expected to be average to below average.
Streamflow in the Sheri River is expected to be well above average, mostly due to runoff from the northern catchment of Lake Malawi (Tanzania).
Zambezi
Kafue
Luangwa
Sheri

## Slide 32: Seasonal Streamflow Forecast
GloFAS seasonal forecast Jan - Apr 2024
GloFAS monthly forecast (Jan – Apr 2024)
Zambezi
Kafue
Luangwa
Sheri
A
@ point A: Sheri River near Blantyre
Above average streamflow in the Sheri River.
Flooding may occur in southern Malawi (same areas affected by flooding in March of 2023 due to TC Freddy).

## Slide 33
Thank you
Questions?