## Slide 1: Irrigated Area Modeling & Mapping
Applications of FEWS NET Remote Sensing products for Agro-climatological Analysis Workshop
10 – 14 July 2017 | Kathmandu Nepal

## Slide 2
Two major growing seasons for irrigated crops
Irrigated area in eMODIS Normalized Difference Vegetation Index (NDVI)
Can we use NDVI to map irrigated area?
Irrigated Area Model

## Slide 3
We developed a geospatial model which thresholds the seasonal NDVI in a decision tree algorithm
Thresholds vary by location/province
Irrigated Area Model
Pervez et al., 2014
http://www.sciencedirect.com/science/article/pii/S0034425714001461?via%3Dihub

## Slide 4
NDVI response to water availability
Dry condition
Wet condition

## Slide 5
Spatial variability of water availability
2013-2014 snow water volume by basin

## Slide 6
Irrigated Area Model Optimization
Model was optimized for normal, wet, and dry conditions specific to the sub-basin level
Run time: beginning of October
Irrigated area map was produced for the years 2002 to 2016

## Slide 7
How Accurate were the Maps?
Landsat image, April 2010
Landsat derived irrigated areas, 2010
Comparison with irrigated area derived from Landsat

## Slide 8
Correlation with Cereal Production
Total cereal production was highly correlated with the amount of area irrigated each year

## Slide 9
Estimated cereal production for 2016: 6.3 M MT
Early Estimation of Crop Production
Year | Irrigated Areas (mHa) | Estimated Cereal Production (mMT) | Reported Cereal Production (mMT)
2001 | 1.34 | 1.95 | 1.98
2002 | 1.64 | 3.74 | 3.59
2003 | 1.93 | 5.05 | 5.37
2004 | 1.52 | 3.07 | 3.06
2005 | 2.15 | 5.77 | 5.24
2006 | 1.73 | 4.17 | 4.80
2007 | 2.15 | 5.78 | 5.64
2008 | 1.71 | 4.05 | 3.65
2009 | 2.27 | 6.08 | 6.33
2010 | 2.05 | 5.48 | 5.59
2011 | 1.92 | 5.01 | 4.44
2012 | 2.10 | 5.64 | 6.32
2013 | 2.42 | 6.46 | 6.51
2014 | 2.54 | 6.10 | 6.74
2015 | 2.41 | 6.31 | 5.80
2016 | 2.51 | 6.3 | 
Crop production estimate was possible by October for the current year

## Slide 10
Modeled vs Reported Production

## Slide 11
It is fair to assume that most areas irrigated in the second season was irrigated in the first season (True?)
Early Estimate of Crop Production
Can we map irrigated areas after the first season?
Currently provides production estimate by October

## Slide 12
First Season Irrigated Area Map
Irrigated area model was recalibrated
Run time: early June
Season’s end (October)
After first season (June)

## Slide 13
First Season Irrigated Area
First season irrigated area in comparison with season end irrigated area and cereal production

## Slide 14
Early Estimation of Crop Production
A regression equation relating crop production estimates by June to historical cereal production was applied for estimating 2017 production.
Estimated cereal production for 2017 is 6.36 M MT

## Slide 15: Questions?