## Slide 1: Satellite Rainfall Estimates RFE & CHIRPS
Applications of FEWS NET Remote Sensing products for Agro-climatological Analysis Workshop
10 – 14 July 2017 | Kathmandu Nepal

## Slide 2: Rainfall Monitoring – 2 Primary Sources
1) NOAA CPC/Rainfall Estimates (RFE2.0)
  Coverage: Africa, South/Central Asia
  RFE 2.0 (daily estimates) from 2001-present
    GOES Precipitation Index (GPI) from Infra-red cold cloud duration)
    Incorporation of microwave from AMSU-B and SSM/I
    Incorporation of GTS rain gauge data
2) USGS/UCSB CHIRPS (Climate Hazards Group InfraRed Precipitation with Stations)
  Coverage: Global – 50 deg N to 50 deg S
  CHIRPS 2.0 (pentadal estimates) 1981-present
    CHPClim monthly rainfall long-term averages
    Cloud top temperatures (Satellite thermal-infrared data from NOAA)
    Rain gauge data from a variety of sources

## Slide 3: NOAA CPC RFE2: Basic Assumptions
Much of the rainfall in the tropics comes from convective storm clouds
These clouds precipitate when their tops have reached a certain optimal temperature or height
The cloud top temperature (related to height) can be computed from satellite infra-red (IR) images derived from observational data

## Slide 4: RFE: GOES Precipitation Index Technique
Cold cloud duration threshold (235K or -38deg. C)
Assumed rate of 3 mm/hour

## Slide 5: RFE: Microwave Inputs (SSM/I & AMSU-B)
SSM/I (stratospheric sounding microwave/imager)
2 instruments estimate precipitation daily at ~6 hourly frequency
Tends to sharply overestimate detected convective rainfall
Fails to catch other rainfall in temporal gaps
AMSU-B (advanced microwave sounder)
Data available 4 times daily, staggered temporally
Tends to overestimate most precipitation, but does well with highly convective systems
Pre-processing of data; conversion from HDF format and resampling to 0.1 deg resolution

## Slide 6
Synergy of Outputs for
Final Product
The three satellite estimates are combined linearly using predetermined weighting coefficients, then merged with the GTS station data.

## Slide 7: RFE: Characteristics
Spatial:
  0.1 degree (~10km) pixel resolution
  Africa, Central Asia, South Asia coverage
Temporal:
  Daily estimates, summed to dekadal (approx 10-day) totals
  2001-present
Quantities:
  Units: mm
Typical Presentation:
  Actual, Diff-Avg, Pct-Avg, graphs, 30-day rain/dry day
Accuracy:
  Estimates convective rainfall best
  Good when rain gauges available on GTS

## Slide 8
Daily RFE

## Slide 9
Daily GFS Forecast

## Slide 10
Dekadal (10-day) RFE

## Slide 11
Dekadal (10-day) RFE

## Slide 12
Dekadal Cumulatives

## Slide 13
Other Dekadal Cumulatives

## Slide 14: RFE– strengths and limitations
Strengths:
  Provides good spatial representation of rainfall performance
  High native temporal resolution (daily): allows further analysis at a daily time step (e.g. dry spells)
  Can be improved after the final product using locally available rain gauge data

## Slide 15: RFE– strengths and limitations
Limitations:
  Cirrus clouds (cold and non-raining clouds)
  Coarse resolution – misses very isolated storms
  Does not perform very well where there are no rain gauges reporting on the GTS network or when GTS station reporting is irregular

## Slide 16
Climate Hazards Group InfraRed Precipitation with Stations (CHIRPS) Dataset
https://pubs.er.usgs.gov/publication/ds832

## Slide 17: CHIRPS Process
Create historic precipitation climatology CHPclim
Convert IR data to precipitation estimate IRP
  IRP = b0 + b1 *(Cold Cloud Duration percent)
Apply time variability of IRP to CHPclim to make CHIRP
  CHIRP = CHPclim * (IRP %normal)
Blend in stations with CHIRP to make CHIRPS

## Slide 19: Station density

## Slide 20
Total rainfall from Apr-Sep 2014 (Ethiopia mean [mm])
Precipitation Sources:

## Slide 21
Comparison with Independent stations.

## Slide 22
Monthly Station Stats by Source

## Slide 23: CHIRPS: Characteristics
Spatial:
  0.05 degree (~6km) pixel resolution
  Global coverage, with windows available for select geographical areas (including Africa, Central Asia, Central America, Caribbean, SE Asia)
Temporal:
  Pentadal, dekadal and monthly estimates available
  1981-present
Quantities:
  Units: mm
Typical Presentation:
  Actual, Diff-Avg, Pct-Avg, SPI, graphs
Accuracy:
  Improves with more rain gauge data available

## Slide 24
CHIRPS Products
Monthly Precipitation – May 2017
Monthly Anomaly – May 2017

## Slide 25
CHIRPS Products
3-Monthly Prec. – MarAprMay 2017
3-Monthly Anom – MarAprMay 2017

## Slide 26: CHIRPS – strengths and limitations
Strengths:
  Provides good spatial representation of rainfall performance
  Provides superior spatial resolution (0.05 deg) in comparison to other rainfall datasets
  Global extent
  Based on a long-term (1981-present) climatology, allowing for rainfall trend analysis
  An abundance of station data is incorporated

## Slide 27: CHIRPS – strengths and limitations
Limitations:
  Pentadal (5-day) data disaggregated to daily observations
  Timeliness of “final” data – prelim for operational
  Tends to miss high rainfall events due to being tuned as a drought indicator

## Slide 28: Rainfall data and tools: where to access
USGS FEWS NET Data Portal
  http://earlywarning.usgs.gov/fews
  GIS Data, graphics, charts,
Early Warning Explorer:
  http://earlywarning.usgs.gov/fews/
  Web-mapping, charts, graphics
GeoWRSI and GeoCLIM (variable accumulation periods, country specific windows)
  http://chg.geog.ucsb.edu/tools/
CHIRPS data downloads
  ftp://chg-ftpout.geog.ucsb.edu/pub/org/chg/products/CHIRPS-2.0/

## Slide 29: Questions?