## Slide 1: Normalized Difference Vegetation Index (NDVI) MODIS to VIIRS Transition
Mike Budde
Science Meeting – Boulder, CO
13-15 June 2023

## Slide 2
  TERRA
  Launched Dec 1999
  6-year design life
  Morning – 10am overpass
  AQUA
  Launched May 2002
  6-year design life
  Afternoon – 1pm overpass
  The MODIS instruments aboard both EOS satellite platforms has provided NDVI source data for more than 20 years.
  Both platforms will be decommissioned over the course of the next year – therefore an alternative source for these data was needed.
  EROS stopped processing eMODIS as of September 2022.

## Slide 3
  Suomi National Polar-orbiting Partnership (Suomi-NPP)
  Launched Oct 2011
  JPSS is the next generation of polar-orbiting Earth observing satellites and will ultimately include 5 satellites with varied instrumentation.
  JPSS-2
  Launched Nov 2022
  JPSS-3 – Launch 2028
  JPSS-4 – Launch 2032
  Each of these satellites will include an instrument called Visible Infrared Imaging Radiometer Suite (VIIRS) which is the replacement for MODIS.
Joint Polar Satellite System (JPSS) Program
  NOAA-20 (JPSS-1)
  Launched Nov 2017

## Slide 4: eVIIRS NDVI – Operational Monitoring
  FEWS NET Regional Windows – Africa, Central Asia, Central America/Hispaniola, South America, & Australia/Indonesia

## Slide 5: Sensor Characteristics Comparison
Spatial:
  250m pixel resolution
  Global daily coverage
Temporal:
  10-day (dekadal) composite
  Updated every 10 days
  Afternoon overpass
Spatial:
  375m pixel resolution
  Global daily coverage
Temporal:
  10-day (dekadal) composite
  Updated every 5 days
  Afternoon overpass
Accuracy:
  Cloud – smoothing
eMODIS (2003-Sept 2022)
eVIIRS (2012-present)
Accuracy:
  Cloud – modified smoothing
  Higher quality in general

## Slide 6: NDVI Dekad 16/Pentad 32

## Slide 7: NDVI Percent Anomaly Dekad 16/Pentad 32
2022 / Median (2003-2017)
Period 16 / Jun 01-10,2022
2022 / Mean (2012-2021)
Period 32 / Jun 01-10,2022

## Slide 8: Extending our NDVI History of Record Translated eMODIS to match eVIIRS – Geometric Mean Regression
Greater Horn of Africa Seasonal Comparisons 2017-19

## Slide 9: Extending our NDVI History of Record Translated eMODIS to match eVIIRS – Geometric Mean Regression
The entire eMODIS record from 2003-2011 has been transformed to match eVIIRS and is being referred to as eVMOD.
eVMOD has been used along with the 2012-2022 record of eVIIRS to generate a 20-year mean period (2003-2022).
The eVMOD/eVIIRS 20-year mean is operational in EWX as a secondary mean source when viewing NDVI time series.
The eVMOD/eVIIRS is also being developed as a stand alone NDVI product that generates our standard anomaly and percent of mean anomaly based on the 20-year period.

## Slide 10: eVIIRS in EWX Time series plots have both a 20-year and 10-year mean option

## Slide 11: Extending our NDVI History of Record 10-Year Mean (2012-2021) and 20-Year Mean (2003-2022)

## Slide 12: Extending our NDVI History of Record 10-Year Mean (2012-2021) and 20-Year Mean (2003-2022)

## Slide 13: Extending our NDVI History of Record 10-Year Mean (2012-2021) and 20-Year Mean (2003-2022)

## Slide 14: Extending our NDVI History of Record 10-Year Mean (2012-2021) and 20-Year Mean (2003-2022)

## Slide 15: Extending our NDVI History of Record 10-Year Mean (2012-2021) and 20-Year Mean (2003-2022)

## Slide 16: Extending our NDVI History of Record 10-Year Mean (2012-2021) and 20-Year Mean (2003-2022)

## Slide 17: Summary
Two NDVI data streams will be maintained.
                - VIIRS only that currently uses a 10-year mean
                - Translated MODIS/VIIRS that uses a 20-year mean
EWX and EWX Lite tools both provide the two mean periods for time series analysis.
Time series for the two mean periods can identify changes in timing of start of season as well as changes in the amplitude of the seasonal signal.
With the scheduled follow-on missions for the satellites carrying the VIIRS sensor, we should be able to utilize these data to provide NDVI for FEWS NET well into the next decade.

## Slide 18: Thank You